## Slide 1
The implementation of an MRV system for Land Transport in Morocco
Transport and Climate Change Week 2024
Methodology & Results
08 November 2024 | Rabat
Presented by: Karim Ben Amara
Head of Sustainable Mobility Service – Road Transport Directorate | Ministry of Transport and Logistics

## Slide 2
BACKGROUND : WHY AN MRV SYSTEM ?
Lack of accurate data and indicators on vehicle activity, energy footprint by transport sector, GHG emissions from land transport and their breakdown by sector...
Complexity in identifying mitigation niches, designing and evaluating mitigation measures and improving energy efficiency…
Measures and projects adopted without any assessment of their impact on energy consumption and GHG emissions.
Ensure the effectiveness of investments in this area
Meet transparency requirements regarding the Kingdom’s commitments
Improve credibility with (green) donors
2
1
3
4
Prioritising and targeting actions
Better design, plan and implement actions
Assess and Adjust
Identifying niches for mitigating and improving EE

## Slide 3
APPROACHES TO GHG CALCULATION
Bottom-up
Based on detailed data on transport activities
Top-down
Based on national energy consumption
Fuel
Consumption
Emission Factor
(gCO2/litre)
(gCO2/TJ)
GHG Emissions
(CO2)
Number of vehicles
Emission Factor
(CO2/ litre)
Fuel Consumption (litre/100km)
Average
travelled Distance
(km/an)
GHG Emissions
(CO2)

## Slide 4
METHODOLOGY ADOPTED
Governance
Setting-up of the working group; consultation of stakeholders
Data collection
Identification of sources and data collection (fleets, mileage, etc…)
Data process
Programming of database processing code
Analysis & Inventary
« Bottom-up » analysis of activity data and GHG emissions
01
02
03
04
Integration & Sustainability
Integration with existing systems and input into official communications
05

## Slide 5
METHODOLOGY ADOPTED : STEP 1
Governance
Setting-up of a working group; stakeholder consultation
Collecte
des données
Identification des sources, et collecte des données (flottes, kilométrages,…)
Traitement des données
Programmation d‘un code pour le traitement des bases de données
Analyse & Inventaire
Analyse des données d’activités et des émissions GES « bottom-up»
01
02
03
04
Intégration & pérennisation
Intégration dans les systèmes acuels et alimentation des communications officielles
05

## Slide 6
PROJECT TEAM
PARTIE CONCERNEE & COMITE CONSULTATIF
Ministry of Interior (DGCT);
Ministry of Equipment and Water (CNER);
Ministry of Energy Transition and Sustainable Development;
Mohammed VI Fondation for Environnemental Protection;
National Railways Office (ONCF);
National Transport and Logistics Company (SNTL);
Association of Vehicles Importers in Morocco (AIVAM)
Ben Amara Karim
Benniss Fairouz
Zemani EL Mustapha
ElMir Oussama
Naciri Ikram
Anne Sophie Tobar-Malagueno
Medrari Hicham
Flues Verena
Khatiri Fatima

## Slide 7
METHODOLOGY ADOPTED: STEP 2
Gouvernance
Formation du groupe de travail; consultation des acteurs
Data collection
Identification of sources and data collection (fleets, mileage, etc…)
Traitement des données
Programmation d‘un code pour le traitement des bases de données
Analyse & Inventaire
Analyse des données d’activités et des émissions GES « bottom-up»
01
02
03
04
Intégration & pérennisation
Intégration dans les systèmes acuels et alimentation des communications officielles
05

## Slide 8
DATA COLLECTION

## Slide 9
DATA COLLECTION
12
million
Periodic technical inspections of vehicles over 5 years
+6
million
Registrations and identifications
160 000
Technical inspections for 2/3-wheeler
Type, use, Gross vehicle weight, number of seats,
Categorization of vehicles in categories M1, M2, M3, N1. etc.
Date of technical inspections and mileage on the odometer
Average annual mileage by vehicle class and active vehicles
Type of fuel
Breakdown of kilometres by fuel type
Registration date
And circulation date
Average age by vehicle category

## Slide 10
METHODOLOGY ADOPTED : STEP 3
Gouvernance
Formation du groupe de travail; consultation des acteurs
Collecte
des données
Identification des sources, et collecte des données (flottes, kilométrages,…)
Data processing
Programming of database processing code
Analyse & Inventaire
Analyse des données d’activités et des émissions GES « bottom-up»
01
02
03
04
Intégration & pérennisation
Intégration dans les systèmes acuels et alimentation des communications officielles
05

## Slide 11
DATA PROCESSING
Cleaning
Plausibilisation and first general analysis of databases (registration, technical inspection, state vehicles, etc.)
Database cleanup: Correction of input errors, Format alignment
Determination of the actual number of motorized road vehicles actually running in Morocco: Who passed the periodic technical inspection + less than 5 years old
The initial database includes multiple uses and types of vehicles translated by the Technical WG into 10 official categories (BO)
1st analysis
Active fleet
Catégorisation
2
1
3
4

## Slide 12
DATA PROCESSING
Algorithm developped by Python to process millions of data (supported by IFEU)
Capacity-building for the team through training sessions in (Data science & big data) using the Python programming language

## Slide 13
METHODOLOGY ADOPTED : STEP 4
Gouvernance
Formation du groupe de travail; consultation des acteurs
Collecte
des données
Identification des sources, et collecte des données (flottes, kilométrages,…)
Traitement des données
Programmation d‘un code pour le traitement des bases de données
Analysis & Inventory
« Bottom-up » analysis of activity data and GHG emissions
01
02
03
04
Intégration & pérennisation
Intégration dans les systèmes acuels et alimentation des communications officielles
05

## Slide 14
Main results : vehicles fleet in Morocco
 | Registered fleet1 | Active fleet2 | Average age | Kilometres travelled3 | Energy consumption4 | GHG Emissions5
 | 6.2 M vehicles | 5.4 M vehicles | 13 years | 79 Mds kilometers | 6 212 (1000 TEP) | 19.3 M Tonne CO2eq

## Slide 15
Annual mileage travelled by vehicles

## Slide 16
GHG Land transport emissions

## Slide 17
Carbon footprint by vehicle category

## Slide 18
Verification of results
There is some uncertainty in the input data, in particular the average fuel consumption values by vehicle category;
The difference in the results between the energy balance and the inventory carried out is 1% for diesel (the majority of the fleet);
Good validation result through comparison of energy consumption values in road transport;

## Slide 19
Main Conclusions & Recommendations
Main conclusions
Motorized land mobility is dominated by private vehicles. The latter accounted for more than half of the sector's GHG emissions in 2022; Two- and three-wheeled motor vehicles accounted for more than 25% of the kilometres travelled by all motorised vehicles (including trains) in 2022; The significant environmental potential of rail transport; Regarding the transport of goods, the largest carbon footprint is that of category (N2) trucks;
Recommendations
The need to rationalise travel and the individual use of motorised private cars (by encouraging carpooling, for example); The modal shift towards micro-mobility and public transport; The modal shift from road freight transport to rail or sea transport; Improving the energy and environmental efficiency of vehicles;

## Slide 20
METHODOLOGY ADOPTED : STEP 5
Gouvernance
Formation du groupe de travail; consultation des acteurs
Collecte
des données
Identification des sources, et collecte des données (flottes, kilométrages,…)
Traitement des données
Programmation d‘un code pour le traitement des bases de données
Analyse & Inventaire
Analyse des données d’activités et des émissions GES « bottom-up»
01
02
03
04
Integration & sustainability
Integration with existing systems and input into official communications
05

## Slide 21
Procéder à la réalisation de la deuxième édition de l’Inventaire des émissions des GES du secteur des transports terrestres au titre de l’année 2023 en améliorant certaines données et en produisant d’autres types d’indicateurs (par sous branche de transport / urbain & non-urbain)
SUSTAINABILITY & IMPROVEMENT
Mise en œuvre des conventions signées aujourd’hui & en tenant la 1ère réunion des instances de gouvernance

## Slide 22
NEXT STEPS
Publication of the final report detailing the methodology, the main findings, the indicators and the recommendations for 2022
Publication of a summary presenting the important results, indicators and recommendations

## Slide 23
NEXT STEPS
Implement recommendations by adopting the same participatory approach, involving all the parties concerned.
IMPROVE : Introducing Measures, Pathways and Roadmaps for Optimizing Vehicle Efficiency